## Slide 1: MASTER CONTROLLER WITH SHARED CONTROL FOR A CONTINUUM ROBOT
Shen Treratanakulchai
Supervisor
Prof. Guang-Zhong, Yang

## Slide 2: Outline
Introduction
Literature Review
Material & Methods
Preliminary Study
Gantt Chart

## Slide 3: Introduction
Minimally Invasive Surgery
Natural Orifice Transluminal Endoscopic Surgery (NOTES)
  Small/ No incision
  Less trauma + Fast recovery
  Less Infection
Constrain
  Confined workspace
  Small and highly flexible Instrument only
  Surgical Remotely
https://www.kisspng.com/png-muscle-human-body-anatomy-homo-sapiens-omega-3-fat-721162/preview.html
Transoral Surgery
Transnasal Surgery
Transluminal Surgery
Transumbrical Surgery
Cardiovascular Surgery
Colorectal cancer is 1/3 of commonly cancer [1] US: ~51,000 Persons oral cavity cancer with estimated 10,000 deaths in 2018[2]
[1] J. Shang et al., “A Single-Port Robotic System for Transanal Microsurgery—Design and Validation,” IEEE Robotics and Automation Letters, vol. 2, no. 3, pp. 1510–1517, 2017
[2] US National Cancer Institue

## Slide 4: Introduction(cont.)
Continuum Robot
  Flexible shape instrument (Snake-like robot)
  Replacing Rigid-endoscope instrument
  Allow navigation & surgery in confined space
  Bi-Manual manipulation
  Master/Slave Teleoperation
  High redundant DOFs
Main Body
Instrument

## Slide 5: Introduction(cont.)
Available Master Controller
  Master-Slave Teleoperation system
  End-effector(Tip) pose control
  Haptic sensation feedback

## Slide 6: Introduction (cont.)
Limitations of the commercial master device for a continuum robot
  No intermediate Joint Shape Control
  Main robot control and instrument control are controlled separately
  Lack of sense of touch for object manipulation and intermediate joint compliance
  The mismatch kinematic in master/slave teleoperation system
    Different number degree of freedoms (Master:LowDOF -> Slave:HighDOF)
    Workspace mismatch -> Required Clutching
  Commercial available device have not developed for the continuum robots
  Hand-Eye Coordination Problems

## Slide 7: Introduction (cont.)
Objectives
  To develop the master controller for a continuum surgical robot more intuitive
  To develop a master controller with shared control architecture
  To develop master controller as a haptic device with transparency properties.
  To control the slave robot with smooth movement and provide maximum exert force in particular direction using the auxiliary algorithm
Expected Results
  Intuitive device for continuum robot control by design and assistive algorithm
  Realistic haptic feedback providing for the NOTES application in shared control architecture

## Slide 8: Literature Reviews
Surgical Robot In NOTES
  Tendon driven based
    No external force sensing
  Concentric Tube
    Precurvature and length
  Instrumentation- visualization and Surgical integration
da Vinci Xi

## Slide 9: Literature Reviews(cont.)
Hamlyn Centre Previous Works
  Micro-IGES robot system for TEMS
  Rectum Surgery
Joint Mapping Controller
Parallel Master Controller (Omega 7)
 | Joint Mapping Controller (Piyamate's design) | Parallel Master Controller (Omega 7)
Maximum lateral Force | 5N | 12 N
Inertia | High | Low
Dynamics (Force/Velocity) | Low | High
Kinematic | -Similar to a slave robot -FWD Kinematic: Easy -INV Kinematic: joint mapping | - Dissimilar to a slave robot - FWD Kinematic: difficult - Inv Kinematic: Easy
Workspace scale | - scale 5:1 continuos movement - Large | Clutching to shift Ref. frame - Limitation workspace
# joints | 1 Translational Joint 5 Rotational joints | 6 Rotational Joint 1 Grasping
Workspace/Robot size | High | Low
Stiffness | Low | High
Require force sensor for control | Yes | No
Micro-IGES
Dual 7 DOFs Instrument
Robot Workspace

## Slide 10: Literature Reviews(cont.)
Hamlyn Centre Previous Works
  I2Snake robot system for Transoral Endoscopic Microsurgery
  Oralarynx surgery
I2Snake – Kuka Robot 7 DOFs Instrument
I2Snake – Kuka Robot Dual 7 DOFs Instrument2
 | Oculus Rift | TrakSTAR Interface | Parallel Master Controller
Type | Ungrounded Controller | Ungrounded Controller | Grounded Controller, Stationary
Kinematic | Position and Orientation relative movement | Position and Orientation absolute movement | Position and Orientation relative movement
Workspace | - Open Workspace - limited by line of sight - Require Clutching | - Open Workspace - interfere by the ferromagnetic - No Clutching require | - Constrained Workspace - Clutching requires
Dynamics | - Only Vibration - No Kinaesthetic feedback | - No Vibration - No Kinaesthetic Feedback | - No Vibration - Haptic Feedback
Weights | Lightweight | Very lightweight | High weight
Wiring | Wireless Communication | Wire Connection | Mechanical Linkage
Global Positioning | Clutching | Absolute Control | Clutching

## Slide 11: Material & Methods
Workspace Analysis
Design Optimization based on Force/Velocity manipulability ellipsoid
Dexterity measurement -> Changing velocity ability on both translation VS rotation
-> Changing force ability
Cooperation manipulability
- Measure how to measure coupling motion force/velocity manipulability
- Relative Force/Velocity between robot-human arm or task space
- Design consideration based on mutual manipulability
- Intersecting Ellipsoid Volume
- Mutual manipulability ellipsoid shape
Can’t move much in this direction
Can move a lot in this direction
SVD(J)
V1
V2
Velocity Ellipsoid
Force Ellipsoid
SVD()
Manipulability Ellipsoid of Robot1
Manipulability Ellipsoid of Robot2
Cooperation Manipulability (Intersection Ellipsoid

## Slide 12: Material & Methods(cont.)
Haptic Control
  Impedance control(Instrument)/Admittance control(Robot)/Hybrid control(Instrument+Robot)
  Shared control
  Transparency Design approach
    Gravity compensation
    Frictionless
    High fidelity
    Isotropic Manipulability
Auxiliary and shared control algorithm for continuum robot control
System Integration & Validation

## Slide 13: Expected Outcome
Robot Model Control Global View (Augmented Reality)
Robot First Person View
Robot-Tissue Force interaction
Hand-Robot Force Interaction
Curvilinear Shape Control
Autonomously Path Following
Steerable Section
Instrument Only
Surgical Manipulation
Fixed Camera view
Instrument + Robot
Combined Force(Instrument + Robot)
  Whole manipulator control
Alter Camera View
Robot Only
Navigation Exploration
  Pan/Tilt + FWD/BWD
Object Motion Compensation

## Slide 14
Expected Outcome